## Slide 1: CALIBRATION FOR HISTORICAL CROP ET ESTIMATES
Introduction and Issues
Evapotranspiration Workshop
March 12, 2010
Ft Collins CO
Thomas W. Ley, PhD, PE

## Slide 2: Why Calibration?
Most historical consumptive use analyses based on long evaluation period
Long periods of record available at many NOAA Coop Observer network (max/min/precip) stations
Simple temperature-based methods
Limited period of record at electronic weather stations (20 years or less)

## Slide 3: Why Calibration?
Published studies have generally shown the simpler temperature-based ET estimation methods are inaccurate, especially in arid and semi-arid climates
Local calibration/verification is strongly recommended to obtain more accurate historical crop ET estimates

## Slide 4: Approach
Compute calibration coefficients for some specific time interval during growing season (e.g., 10-days, monthly)
    Measured Crop ET
    Calibration coeff. =
    Crop ET by method being calibrated
In the absence of measured ET (i.e., lysimeter), use crop ET based on ASCE Std Ref-ET Eqn

## Slide 5: Measured Crop ET
Lysimetry
ASCE Std Reference ET
Air temperature
Relative humidity
Wind speed
Rainfall
Solar radiation
Holly02 CoAgMet Station
July 2005
Wind direction

## Slide 6: Approach
Compute average calibration coefficient values for overlapping period of record
  Monthly time step
Minimum 5-7 years of overlapping record

## Slide 7: Modified Blaney-Criddle Method (TR-21)
u = kc (kt) (t x p) / 100
u = monthly consumptive use (inches)
kt = climatic coefficient
= 0.173 * t - 0.314
kc = crop growth stage coefficient
t = mean monthly air temperature (°F)
p = monthly percentage of annual daylight hours

## Slide 8
Data required--mean monthly temperature
100’s of max/min/precip stations in Colorado
Developed for irrigation planning
kt (t * p) / 100 not representative of the impact of meteorological elements
Modified Blaney-Criddle Method

## Slide 9: Extraterrestrial Radiation & Percent of Daylight as a Percentage of Maximum

## Slide 10
Crop factor, kc , is not a crop coefficient in the same sense as the reference ET-crop coefficient approach
Contains a meteorological component
  location bias
  values not geographically transferable (ASCE Manual 70, 1990; USDA-NRCS, 1993)
Ignore kc and calibrate just the factor: kt (t * p) / 100
Modified Blaney-Criddle Method

## Slide 11: 1985 Hargreaves Method
ETo = grass reference ET (mm/day)
Tmax = maximum daily air temperature (°C)
Tmin = minimum daily air temperature (°C)
Tmean = mean daily air temperature
= (Tmax + Tmin) / 2
Ra = extraterrestrial radiation (mm/day)
Ra (mm/day) = Ra (MJ/m2/day) / 2.45

## Slide 12: 1985 Hargreaves Method
Originally developed in 1975
  solar radiation and temperature data inputs
Updated in 1982 and 1985
  solar radiation estimated from extraterrestrial radiation, RA
Grass reference ET
May be used to compute daily estimates, but more accurate over longer time steps: 10-days, monthly

## Slide 13: 1985 Hargreaves Method
Simple, easy to use
Data required—maximum and minimum air temperature
Better predictive accuracy in arid climates than modified Blaney-Criddle
  Max-min temperature difference
  Extra-terrestrial radiation
Underpredicts in windy or high advection conditions—requires local calibration

## Slide 14: 1985 Hargreaves Method
Grass reference ET method
Directly calibrate:
ASCE std ref ETr
K =
Hargreaves ETo
Use alfalfa reference crop coefficients
ETc = Kcr (K * ETo)

## Slide 15: Calibration Precautions/Limitations
Extent of areal representation ?
Weather station pairing
  Compute calibration coefficients by pairing each NOAA station of interest with electronic weather station
  Site bias at the NOAA site may not be properly captured
  Bigger problem with SCS BC than 1985 Hargreaves

## Slide 16
  Coefficients for one EWS-NOAA station pair generally not applicable at other NOAA stations when conditions at the NOAA sites are dissimilar
Rocky Ford CoAgMet
Rocky Ford NOAA
Las Animas NOAA
La Junta NOAA